# Blood Pressure Sensor

## Product Number: ENBLD098

### Overview

The heart is essentially a pump using pressure to move blood through our circulatory system of veins and arteries.  The Blood Pressure Sensor measures the intensity of this pressure on our arteries.   While the heart needs pressure to circulate blood, too much can damage the arteries.

Blood pressure readings consist of two parts - the systolic reading which measures pressure as the heart contracts and forces blood through the system and the diastolic, taken when the heart is at rest.   The systolic is always the higher of the two readings.

Blood pressure varies from person to person and can be affected by factors such as age, height, gender, and diet.

The Blood Pressure Sensor can be connected to all types of einstein™ data loggers.

It can be used for various Biology experiments.

### Typical experiments

Human Physiology

Measure blood pressure before or after exercising

See the difference in blood pressure between different age groups and genders

Investigate how blood pressure changes during the day

Study how certain foods affect blood pressure

### How it works

Blood pressure readings are usually taken from a person's upper arm using a cuff and are expressed in terms of the systolic pressure over diastolic pressure. For example a reading of 120/80 is often generally considered normal.

### Sensor specification

| Heart Rate |  |
| --- | --- |
| Range: | 36 to200 bpm |
| Accuracy: | 1 bpm |
| Blood Pressure |  |
| Range | 0 to 375 mmHg |
| Accuracy | ± 3 mmHg |
| Typical Response Time: | 90 seconds |
| Units: | mmHg |
| Temperature Compensation: | 0 °C to 50 °C |
| Maximum pressure without permanent damage: | 1030 mm Hg |

Note: sensor cables sold separately

### Technical Notes

The Blood Pressure sensor was designed only for educational purposes and should not be used for industrial, medical, or research applications.

### Calibration

The Blood Pressure Sensor is shipped fully calibrated.

### Data logging and analysis

MiLAB™

- Take your einstein™ Tablet OR pair your einstein™LabMate with your Android or iOS tablet via Bluetooth

- Insert the sensor cable into one of the sensor ports

- Launch MiLAB

- MiLAB will automatically detect the sensor and show it in the Launcher View

- Check the icon next to the sensor (  ) to enable it  for logging

MiLAB™ Desktop

- Pair your einstein™LabMate™ with your PC, MAC, or Linux machine via Bluetooth, or connect it via the USB cable (found in the einstein™LabMate™ box)

- Insert the sensor cable into one of the sensor ports

- Launch MiLAB

- MiLAB will automatically detect the sensor and show it in the Current Setup Summary window

- Click Full Setup, located at the bottom of the Current Setup Summary window to program the data logger’s sample rate, number of samples, units of measurement, and other options

- Click the Run button (  ) to start logging

# An example of using the Blood Pressure Sensor

- Set the sample rate :

- Put the cuff on the upper arm :

- Click the Run button (  ) to start logging.

- Pump the cuff till it very tight. Stop pumping and wait until the reading decreases to 50 mmHg.

Measurement will stop automatically, and a result window will appear:

Note: A video detailing use of the Blood Pressure sensor can be found at: https://www.youtube.com/watch?v=bNJhZaNpFkw

### Troubleshooting

If the Blood Pressure Sensor isn't automatically recognized by MiLAB, please contact Fourier Education's technical support.

### Technical support

For technical support, you can contact the Fourier Education's  technical support team at:

Web: www.einsteinworld.com/support

Email: support@fourieredu.com

Phone (International): +972-3-901-4849 ext. 232

### Copyright and Warranty

All standard Fourier Systems sensors carry a one (1) year warranty, which states that for a period of twelve months after the date of delivery to you, it will be substantially free from significant defects in materials and workmanship.

This warranty does not cover breakage of the product caused by misuse or abuse.

This warranty does not cover Fourier Systems consumables such as electrodes, batteries, EKG stickers, cuvettes and storage solutions or buffers.

©Fourier Systems Ltd. All rights reserved. Fourier Systems Ltd. logos and all other Fourier product or service names are registered trademarks or trademarks of Fourier Systems.  All other registered trademarks or trademarks belong to their respective companies.

ALBERT EINSTEIN and EINSTEIN are either trademarks or registered trademarks of The Hebrew University of Jerusalem. Represented exclusively by Green Light. Official licensed merchandise. Website: einstein.biz